SUPLEMENTARY MATERIAL TO

Synthesis and spectral characterization of 1,2-bis(5-methyl/chloro-1H-benzimidazol-2-yl)ethanols and their Co(II), Pd(II) and Zn(II) complexes

Aydın Tavman*, Demet Gürbüz and Adem Cınarlı

Istanbul University, Faculty of Engineering, Department of Chemistry,

Avcilar, 34320, Istanbul, TURKEY.

1,2-Bis(5-methyl-1H-benzimidazol-2-yl)ethanol (1): Yield: 2.17 g (71%). Colorless solid. M.p.: 190 °C (decomp.). Combustion analysis for C18H18N4O: (Mw=306.36 g/mol): C 70.57, H 5.92, N 18.29; found: C 70.26, H 5.81, N 18.02. Mid- and far-IR (ATR): 3120m,br, 3033m,br, 2923m, 2860m, 2733m,br, 1631m, 1594w, 1537m, 1447s, 1409m, 1307m, 1279m, 1224m, 1089m, 1048m, 1022m, 856m, 794s, 597m, 430m, 410m, 374m, 253m, cm–1. Raman: 3059m, 2925m, 2861w, 1645w, 1589m, 1539m, 1442m, 1376w, 1276s, 1129w, 1021w, 944w, 882w, 759m, 597w, 439w, 300w, 200w, cm–1. 1H-NMR (500 MHz, DMSO-d6, δ): 12.17 (s,br, 2H, NH+NH’, exchangeable with D2O), 7.26 (s,br, 2H, H4+H7), 6.92 (s,br, 1H, H6), 6.13 (s,br, 1H, OH, exchangeable with D2O), 5.32 (s,br, 1H, (CH(OH), 3.33 (s,br, 2H, (CH2(; splits two broad singlets in after D2O: 3.49 s,br and 3.67 s,br), 2.36 (s, 3H, (CH3). 13C-NMR (APT, 125 MHz, DMSO-d6, δ): Quaterner carbons: 157.0 (C2), 152.6 (C2’), 141.1 (C9+C9’), 138.2 (C8+C8’), 131.5 (C5+C5’); H-bonded carbons (CHs): 123.2, 122.4, 67.2 (C(OH), 36.7 ((CH2(), 22.0 ((CH3). Fluorescence spectra (EtOH, c = 1·10–4 mol L(1) λmax / nm: 406m,br, 428m, 456sh. ESI-MS (m/z): 307.2 ([M+1]+, 100), 308.5 ([M+2]+, 32.2), 310.0 ([M+4]+, 7.5), 289.5 ([M-OH)-1]+, 10.4).

1,2-Bis(5-chloro-1H-benzimidazol-2-yl)ethanol (2): Yield: 2.05 g (59%). Colorless solid. M.p.: 212 °C (decomp.). Combustion analysis for C16H12Cl2N4O (Mw=347.20 g/mol): C55.35, H 3.48, N 16.14; found: C 55.26, H 3.31, N 16.11. Mid- and far-IR (ATR): 3145m,br, 3046m,br, 2986w, 1623w, 1585w, 1542w, 1473m, 1444m, 1414m, 1300w, 1086s, 1024m, 927m, 848m, 803m, 599m, 561s, 537m, 475w, 423w, 390m, 272m, 175m, 132m, cm–1. Raman: 3085m, 2943m, 2900w, 1584m, 1539m, 1469w, 1291w, 1276w, 1056m, 998w, 960w, 886w, 805w, 705w, cm–1. 1H-NMR (500 MHz, DMSO-d6, δ): 12.57 (s,br, 1H, NH’, exchangeable with D2O), 12.50 (s,br,1H, NH, exchangeable with D2O), 7.56 (m,br, 1H, H7), 7.53 (s, 1H, H4), 7.14 (d,br, 1H, J = 8.3 Hz, H6), 6.25 (s, 1H, OH, exchangeable with D2O), 5.37 (dd, 1H, J = 8.3, 4.9 Hz, (CH(OH), 3.55 (dd, 2H, J = 14.9, 4.9, (CH2(). 13C-NMR (APT, 125 MHz, DMSO-d6, δ): Quaterner carbons: 159.2 (C2), 154.6 (C2’), 144.7 (C9), 142.7 (C9’), 135.7 (C8), 133.8 (C8’), 126.9 (C5), 126.1 (C5’); H-bonded carbons (CHs): 122.7, 120.6, 118.8, 113.5, 112.9, 111.5, 67.0 (C(OH), 36.8 ((CH2(). Fluorescence spectra (EtOH, c = 1·10–4 mol L(1) λmax / nm: 401m,br, 423m, 451sh. ESI-MS (m/z): 347.3 ([M]+, 100), 348.3 ([M+1]+, 16.7), 349.2 ([M+2]+, 61.7), 350.3 ([M+3]+, 11.7), 351.2 ([M+4]+, 11.4), 369.1 ([M+23(Na)-1]+, 17.1), 313.4 ([(M-Cl)+1]+, 6.8), 279.3 ([(M-2Cl)+1]+, 3.2).

[Co(1)2(H2O)]Cl2·H2O (1a): Yield: 0.188 g (93%). Purple-blue solid. M.p.: 253 °C (decomp.). Combustion analysis for C36H40Cl2N8O4Co (Mw=778.61 g/mol): C 55.53, H 5.18, N 14.39; found: C 54.96, H 5.05, N 14.03. ΛM (DMF, 25 °C): 86 S m2 mol–1. Magnetic moment, µeff,: 4.47 µB. Mid- and far-IR (ATR): 3112m,br, 3036m,br, 2918m, 1630m,br, 1597m,br, 1538m,br, 1455s, 1416m, 1320m, 1283m, 1224m, 1075m, 1056m, 864m, 802s, 597m, 478w, 432m, 429m, 413m, 372w, 122s, cm–1. Raman: 3055m, 2923m, 2865w, 1648w, 1594m, 1539s, 1460m, 1379w, 1283s, 1142w, 1081w, 942w, 763m, 506w, 451w, 242w, 175m, cm–1. Fluorescence spectra (EtOH, c = 1·10–4 mol L(1) λmax / nm: 405m,br, 428m,br, 456sh. ESI-MS (m/z): 307.2 ([ML*+1]+, 100), 670.2 ([(2L+Co)-1]+, 26.9), 705.8 ([(2L+Co+Cl)-1]+, 16.3), 764.0 ([(M-H2O)+3]+, 5.3).

[Pd(1)Cl]2Cl2·2H2O (1b): Yield: 0.180 g (71%). Slightly khaki solid. M.p.: >350 °C (decomp.). Combustion analysis for C36H40Cl4N8O4Pd2 (Mw=1003.41 g/mol): C 43.09, H 4.02, N 11.17; found: C 42.93, H 4.44, N 10.89. ΛM (DMF, 25 °C): 123 S m2 mol–1. Mid- and far-IR (ATR): 3353m,br, 3303m,br, 3227s,br, 3087w, 2923m, 1662w, 1631m, 1600m, 1537m, 1469s, 1285m, 1250m, 1170m, 1075m, 1046m, 857m, 803s, 674m, 597m, 413m, 295m,br, 271s, 134s, cm–1. Raman: 3058m, 2926m, 1598m, 1544s, 1451m, 1381w, 1288s, 1230w, 1056w, 1002w, 956w, 890w, 762m, 650w, 465w, 213w, cm–1. 1H-NMR (500 MHz, DMSO-d6, δ): 13.47 (s,br, 2H, NH+NH’, exchangeable with D2O), 8.73 (s,br, 1H, H7), 8.06 (s,br, 1H, H4), 7.24 (s,br, 1H, H6), 7.22 (s,br, 1H, OH, exchangeable with D2O), 6.77 (s,br, 1H, (CH(OH), 4.77 (s,br, 2H, (CH2(), 2.47 (s, 3H, (CH3). 13C-NMR (APT, 125 MHz, DMSO-d6, δ): Quaterner carbons: 155.4 (C2), 150.5 (C2’), 140.2 (C9), 138.3 (C9’), 134.1 (C8), 133.0 (C8’), 132.5 (C5’), 131.2 (C5); H-bonded carbons (CHs): 125.9, 125.1, 119.4, 112.7, 112.2, 64.8 (C(OH), 35.3 ((CH2(), 19.0 ((CH3). Fluorescence spectra (EtOH, c = 1·10–4 mol L(1) λmax / nm: 373w, 393w. ESI-MS (m/z): 481.0 ([(M/2-H2O)-3]+, 100), 479.0 ([(M/2-H2O)-4]+, 82.6), 477.9 ([(M/2-H2O)-6]+, 69.1), 482.9 ([(M/2-H2O)-1]+, 48.7), 480.0 ([(M/2-H2O)-3]+, 42.1), 476.8 ([(M/2-H2O)-5]+, 21.6), 481.9 ([(M/2-H2O)-2]+, 19.5), 484.9 ([(M/2-H2O)+1]+, 12.1), 307.1 (ML*, 6.1), 717.1 ([M-PdCl2]+, 11.25), 964.02 ([M-2H2O-3]+, 6.21).

[Zn(1)Cl2]·2H2O (1c): Yield: 0.235 g (88%). Colorless solid. M.p.: 309 °C (decomp.). Combustion analysis for C18H22Cl2N4O3Zn (Mw=478.71 g/mol): C 45.16, H 4.63, N 11.70; found: C 44.63, H 3.76, N 11.13. ΛM (DMF, 25 °C): 9.0 S m2 mol–1. Mid- and far-IR (ATR): 3298m,br, 3218m,br, 3059m,br, 2921m, 1627m, 1597m, 1537m, 1463s, 1416m, 1303m, 1228m, 1075m, 1054m, 861m, 798s, 669m, 596m, 550m, 421m, 320s,br, 178m, 142m, 114m, cm–1. Raman: 3065m, 2960w, 2922s, 2867w, 1629w, 1598m, 1532s, 1470w, 1424w, 1377w, 1293s, 1231w, 1138w, 1064w, 1018w, 948w, 871w, 770m, 325m, 290w, 182m, cm–1. 1H-NMR (500 MHz, DMSO-d6, δ): 13.43 (s,br, 2H, NH+NH’, exchangeable with D2O), 8.08 (s,br, 1H, H7), 7.44 (s,br, 1H, H4), 7.21 (dd, 1H, J = 7.0, 4.2, H6), 6.93 (s, 1H, OH, exchangeable with D2O), 5.51 (d, 1H, J = 8.3, (CH(OH), 3.82 (dd, 1H, J1 = 15.6, J2 = 9.3, (CH2(), 3.64 (d, 1H, J = 15.6, 3.82 Hz, (CH2(),2.46 (s, 3H, (CH3). 13C-NMR (APT, 125 MHz, DMSO-d6, δ): Quaterner carbons: 158.2 (C2), 152.8 (C2’), 140.7 (C9), 138.3 (C9’), 134.1 (C8), 133.1 (C8’), 131.0 (C5); H-bonded carbons (CHs): 126.3, 125.2, 118.5, 112.7, 64.7 (C(OH), 35.5 ((CH2(), 22.0 ((CH3). Fluorescence spectra (EtOH, c = 1·10–4 mol L(1) λmax / nm: 375w, 421sh, 442m,br. ESI-MS (m/z): 307.3 ([ML*+1]+, 100), 405.3 ([(L*+ZnCl)-2]+, 99.6), 848.9 ([(2L+2Zn+3Cl)-1]+, 66.3), 409.3 ([(L+ZnCl)+2]+, 65.0), 713.2 ([2L+ZnCl]+, 51.3), 813.1 ([(2L+2Zn+2Cl)-1]+, 25.0), 441.3 ([M-(2H2O)-1]+, 8.9).

[Co(2)2]Cl2·2H2O (2a): Yield: 0.186 g (85%). Purple solid. M.p.: 222 °C (decomp.). Combustion analysis for C32H28Cl6N8O4Co (Mw=860.30 g/mol): C 44.68, H 3.28, N 13.03; found: C 44.09, H 3.43, N 12.82. ΛM (DMF, 25 °C): 105 S m2 mol–1. Magnetic moment, µeff: 4.05 µB. Mid- and far-IR (ATR): 3102m,br, 3036m,br, 2891m, 1624m, 1590m, 1531m, 1446s, 1409m, 1320m, 1280m, 1215m, 1077m, 1063 m, 1047s, 931m, 855m, 801s, 709m, 597m, 541m, 476m, 423m, 367m, 288m, 258m, 198m, 122m, cm–1. Raman: 3071m, 2922m, 1590m, 1530s, 1450m, 1427m, 1334s, 1276s, 1231m, 1064m, 708w, 220w, 150m, cm–1. Fluorescence spectra (EtOH, c = 1·10–4 mol L(1) λmax / nm: 399m,br, 424m,br, 453sh. ESI-MS (m/z): 347.3 ([ML*+1]+, 100), 349.2 ([ML+2]+, 64.0), 381.1 ([ML+23+1]+, 38.3), 408.1 ([(L+Co)+2]+, 16.1), 752.0 ([(2L+Co)-1]+, 4.8), 476.0 ([(L+CoCl2)-1]+, 4.2).

[Pd(2)Cl]2Cl2·2H2O (2b): Yield: 0.219 g (89%). Soil colored solid. M.p.: >350 °C (decomp.). Combustion analysis for C32H28Cl8N8O4Pd2 (Mw=1085.08 g/mol): C 35.42, H 2.60, N 10.33; found: C 35.13, H 2.86, N 9.97. ΛM (DMF, 25 °C): 122 S m2 mol–1. Mid- and far-IR (ATR): 3393m,br, 3189m,br, 3053m,br, 1624m, 1590m, 1534m, 1448m, 1406m, 1307m, 1247m, 1184m, 1084m, 1063 m, 1045m, 947m, 854m, 805s, 713m, 597m, 470m, 415m, 345m, 296s, 223s,br, 129s,br., cm–1 Raman: 3078w, 2931w, 1590w, 1526m, 1457w, 1422w, 1282w, 1228w, 1073w, 987w, 875w, 790w, 712w, 506w, 386w, 234w, cm–1. 1H-NMR (500 MHz, DMSO-d6, δ): 13.77 (d,br, 1H, J = 11.2, NH’, exchangeable with D2O), 13.71 (d,br, 1H, J = 9.8, NH, exchangeable with D2O), 8.19 (m, 1H, H7), 7.70 (m, 1H, H4), 7.49 (m, 1H, H6), 7.17 (s,br, 1H, OH, exchangeable with D2O), 6.65 (s, 1H, (CH(OH), 4.73 (d, 1H, J=4.9, (CH2(), 4.69 (t, 1H, J1 = 4.9, J2 = 2.4, (CH2(). 13C-NMR (APT, 125 MHz, DMSO-d6, δ): Quaterner carbons: 157.4 (C2), 152.8 (C2’), 140.9 (C9), 138.8 (C9’), 133.8 (C8), 132.0 (C8’), 129.0 (C5), 127.8 (C5’); H-bonded carbons (CHs): 124.7, 123.7, 121.4, 119.4, 114.8, 112.8, 64.6 (C(OH), 35.1 ((CH2(). Fluorescence spectra (EtOH, c = 1·10–4 mol L(1) λmax / nm: 375w,br, 393m, 461m,br. ESI-MS (m/z): 520.9 ([(M/2-H2O)-4]+, 100), 519.9 (([(M/2-H2O)-5]+, 62.8), 522.9 ([(M/2-H2O)-2]+, 62.7), 518.9 ([(M/2-H2O)-6]+, 60.1), 522.1 ([(M/2-H2O)-3]+, 40.5), 524.9 ([(M/2-H2O)]+, 28.2), 508.5 ([(M/2-H2O-OH)]+, 21.6), 712.9 (2L*+H2O, 28), 347.3 (ML*, 8.2).

[Zn(2)Cl2] (2c): Yield: 0.204 g (94%). Slightly yellow solid. M.p.: >350 °C (decomp.). Combustion analysis for C16H12Cl4N4OZn (Mw=483.51 g/mol): C 39.74, H 2.50, N 11.59; found: C 40.33, H 2.65, N 11.70. ΛM (DMF, 25 °C): 6.0 S m2 mol–1. Mid- and far-IR (ATR): 3189m,br, 3109m,br, 3043m,br, 2897m, 1624m, 1594m, 1535m, 1449s, 1429m, 1300m, 1223m, 1194m, 1081 m, 1068 m, 1045m, 931m, 851m, 801s, 716m, 597m, 419m, 319m,br, 254m, 205m, 173m, 133m, 107s, cm–1. Raman: 3076m, 2922m, 1629w, 1590m, 1536m, 1428m, 1355w, 1285m, 1246w, 1130w, 1067m, 940w, 716m, 325m, 299m, 167w, cm–1. 1H-NMR (500 MHz, DMSO-d6, δ): 13.68 (s,br, 2H, NH+NH’, exchangeable with D2O), 7.90 (s,br, 2H, H4+H7), 7.41 (m, 1H, H6), 6.94 (s, 1H, OH, exchangeable with D2O), 5.55 (d, 1H, J = 7.3, (CH(OH), 3.85 (dd, 2H, J1 = 16.0, J2 = 9.0, (CH2(), 3.66 (d, 2H, J = 14.6, (CH2(). 13C-NMR (APT, 125 MHz, DMSO-d6, δ): Quaterner carbons: 159.9 (C2), 154.8 (C2’), 137.7 (C9+C9’), 133.5 (C8+C8’), 128.4 (C5), 124.5 (C5’); H-bonded carbons (CHs): 124.3, 122.3, 64.8 (C(OH), 35.4,((CH2(). Fluorescence spectra (EtOH, c = 1·10–4 mol L(1) λmax / nm: 394w,br, 425w,br, 453sh. ESI-MS (m/z): 815.1 ([2M-ZnCl2-OH]+, 100), 837.8 ([(2M-ZnCl2-OH)+Na]+), 44), 723.9 ([(2L*+Na)+6]+, 42.2), 827.1 ([2M-ZnCl2-4]+, 30.7), 714.2 ([(2L+Na)-3]+, 12.7), 347.7 ([ML*]+, 16.9), 477.8 ([M-6]+, 11.1). (*L: ligand).

Figure S-1. Far IR spectra of 2 and [Zn(2)Cl2] (2c) at the 100 – 700 cm–1 range.

Table S-1. TGA data of the complexes (thermal decomposition)

| Temperature (ºC) → | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600 | 650 | 700 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Complex↓ | Mass loss (%) |  |
| 1a | 2.9 | 5.0 | 5.3 | 8.4 | 11.1 | 12.8 | 14.5 | 17.6 | 34.6 | 63.2 | 85.3 | 86.2 | 86.1 |
| 1b | 2.8 | 4.2 | 4.9 | 5.6 | 6.8 | 8.2 | 10.9 | 56.1 | 71.8 | 73.1 | 74.6 | 75.1 | 75.0 |
| 1c1 | 6.5 | 6.8 | 7.0 | 7.4 | 8.3 | 9.6 | 10.5 | 14.1 | 16.4 | 20.6 | 30.1 | 49.4 | 80.1 |
| 2a | 3.4 | 4.9 | 5.3 | 8.3 | 10.4 | 15.5 | 19.2 | 23.6 | 28.4 | 36.2 | 75.7 | 86.5 | 90.2 |
| 2b | 3.9 | 5.3 | 5.6 | 6.0 | 8.4 | 13.8 | 18.3 | 26.1 | 38.0 | 78.2 | 78.2 | 78.3 | 78.3 |
| 2c | 0.8 | 1.1 | 1.5 | 1.9 | 4.4 | 8.0 | 12.7 | 18.3 | 37.6 | 55.6 | 71.3 | 85.7 | 86.1 |

1, 750°C: 85.1%.

# Footnotes

*Corresponding author. E-mail:  atavman@istanbul.edu.tr