Ab initio study of mechanism of forming a spiro-Sn-heterocyclic ring compound by cycloaddition reaction of H2C=Sn: and ethylene

XIAOJUN TANa,*, XIUHUI LU b,*

a School of Biological Science and Technology, University of Jinan, Jinan 250022, People’s Republic of China

bSchool of Chemistry and Chemical Engineering, University of Jinan, Jinan 250022, People’s Republic of China

Abstract: X2C=Sn: (X = H, Me, F, Cl, Br, Ph, Ar…) are new species of chemistry. The cycloaddition reaction of X2C=Sn: are new study field of stannylene chemistry. The mechanism of cycloaddition reaction of singlet H2C=Sn: with ethylene was studied for the first time by using the MP2/GENECP(C, H in 6-311++G**; Sn in LanL2dz) method in this paper. From the potential energy profile, it could be predicted that the reaction has one dominant reaction channel. The reaction rule presented is that the 5p unoccupied orbital of tin in H2C=Sn: sidewise overlap with bonding π orbital of ethylene resulting in the formation of an intermediate. Instability of the intermediate make it isomerises to a four-membered ring stannylene. Because the 5p unoccupied orbital of Sn atom in the four-membered ring stannylene and the π orbital of ethylene forms a (→p donor–acceptor bond, the four-membered ring stannylene further combines with ethylene to form another intermediate, and the intermediate further isomerises to a spiro-Sn-heterocyclic ring compound. Sn in the spiro-Sn-heterocyclic ring compound is combined with adjacent atoms by sp3 hybridization. The results of this study reveal the mechanism of cycloaddition reaction of X2C=Sn: with symmetric π bond compounds.

Key words: H2C=Sn:; four-membered ring stannylene; spiro-Sn-heterocyclic ring compound; potential energy profile

*Correspondence to: X. J. Tan; e-mail: jndxswxy@163.com. X. H. Lu; e-mail: lxh@ujn.edu.cn

1. Introduction

The unsaturated olefins of the main group IV elements(C, Si, Ge) are all active intermediates,1-6 Their cycloaddition reaction were studied,7-13 with the progress of these studies, the study on cycloaddition reactions of unsaturated stannylene should also be mentioned on the agenda. But there has been no published reports about cycloaddition reactions of unsaturated stannylene till now. The unsaturated stannylene (eg X2C=Sn:) are a new chemical species and new study field of stannylene chemistry. In particular, the study of mechanism of their cycloaddition reaction. To explore the rules of cycloaddition reaction between X2C=Sn: and the symmetric (-bonded compounds, H2C=Sn: and ethylene were selected as model molecules in this paper, and the cycloaddition reaction mechanism (considering the H transfer simultaneously) was investigated and analyzed theoretically. The research result indicates the laws of cycloaddition reaction between X2C=Sn: and the symmetric π-bonded compounds. which are significant for the synthesis of small-ring containing Sn and spiro-Sn-heterocyclic compounds. The study extends the research area and enriched the research content of stannylene chemistry.

2. Calculation method

We used the method of Second-order perturbation theory (MP2)14 and Gaussian 09 package to optimize the structure of H2C=Sn: and its cycloaddition reaction with ethylene, its transition state form at the MP2/GENECP(C, H in 6-311++G** ; Sn in LanL2dz) theory level. In order to further confirm the correctness of the relevant species and get the thermodynamic function for the species, vibration analysis are included. Finally, the intrinsic reaction coordinate (IRC) 15, 16 is also calculated for all the transition states to determine the reaction paths and directions.

3. Results and discussion

Theoretical researchs show that the ground state of H2C=Sn:(R1) is a singlet state, its cycloaddition reaction with ethylene (R2) has the following three possible ways:

The geometrical parameters of the intermediates(INT1, INT3), transition states (TS1, TS2, TS2.1, TS3) and products (P1, P2, P2.1, P3) which appear in the above three reactions are given in Fig. 1, the energies are listed in Table 1, and the entropy, enthalpy and Gibbs free energy are listed in Table 2, and the potential energy profile of the above three reactions is shown in Fig. 2.

Fig. 1. Optimized MP2/GENECP(C, H in 6-311++G** ; Sn in LanL2dz) geometrical parameters and the

atomic numbering for the species in cycloaddition reaction between H2C=Sn: and ethylene. Bond lengths

and bond angles are in angstrom and degree, respectively.

TABLE 1. The electronic structure energy (Eese/a.u) and relative energies (ER/kJ mol-1) for the species from MP2/GENECP(C, H in 6-311++G** ; Sn in LanL2dz) method at the 298K and 101325Pa.

| Reaction | Species | MP2/GENECP Eese ER |
| --- | --- | --- |
| aReaction(1) | R1+R2 | -120.76486 | 0.0 |
|  | INT1 | -120.78058 | -41.3 |
|  | TS1 (INT1-P1) | -120.72718 | 98.9 |
|  | P1 | -120.73150 | 87.6 |
| aReaction(2) | R1+R2 | -120.76486 | 0.0 |
|  | INT1 | -120.78058 | -41.3 |
|  | TS2(INT1-P2) | -120.76248 | 6.2 |
|  | P2 | -120.82512 | -158.2 |
|  | TS2.1(P2-P2.1) | -120.71765 | 123.9 |
|  | P2.1 | -120.75656 | 21.8 |
| bReaction(3) | P2+R2 | -199.17164 | 0.0 |
|  | INT3 | -199.18360 | -31.4 |
|  | TS3(INT3-P3) | -199.16216 | 24.9 |
|  | P3 | -199.16806 | 9.4 |

aER=Eese－Eese (R1+R2) , bER=Eese—Eese(P2+R2)

TABLE 2. Entropy(S/ a.u), enthalpy（H/a.u）and Gibbs free energy（G/a.u）for the species from

MP2/GENECP(C, H in 6-311++G** ; Sn in LanL2dz) methods at the 298K and 101325Pa.

| Reaction | Species | H/a.u | S/a.u | G/a.u |
| --- | --- | --- | --- | --- |
| Reaction(1) | R1+R2 | -120.68436 | 1.83010×10-4 | -120.73895 |
|  | INT1 | -120.69667 | 1.31074×10-4 | -120.73577 |
|  | TS1 (INT1-P1) | -120.64511 | 1.19512×10-4 | -120.68076 |
|  | P1 | -120.64842 | 1.23904×10-4 | -120.68538 |
| Reaction(2) | TS2(INT1-P2) | -120.67918 | 1.18527×10-4 | -120.714 |
|  | P2 | -120.73864 | 1.17524×10-4 | -120.77369 |
|  | TS2.1(P2-P2.1) | -120.63781 | 1.17213×10-4 | -120.67277 |
|  | P2.1 | -120.67517 | 1.20096×10-4 | -120.71099 |
| Reaction(3) | P2+R2 | -199.03032 | 2.01150×10-4 | -199.09031 |
|  | INT3 | -199.03946 | 1.52138×10-4 | -199.08484 |
|  | TS3(INT3-P3) | -199.01940 | 1.35050×10-4 | -199.05968 |
|  | P3 | -199.02440 | 1.40081×10-4 | -199.06618 |

Fig. 2. The potential energy surface for the cycloaddition reactions between H2C=Sn: and ethylene with

MP2/GENECP(C, H in 6-311++G** ; Sn in LanL2dz)

The unique imaginary frequency of the transition states TS1, TS2, TS2.1, and TS3 through vibrational analysis are 220.7i, 419.7i, 784.5i and 120.8i, therefore, these transition states can be affirmed as the genuine ones. IRC (with the stepsize of 0.1 amu–1/2 bohr) analysis confirms that TS1 connects INT1 and P1, TS2 connects INT1 and P2, TS2.1 connects P2 and P2.1, TS3 connects INT3 and P3.

According to Fig. 2, it can be seen that reaction (1) consists of two steps: the first one is that the two reactants (R1, R2) form an intermediate (INT1). According to Fig. 2 and Table 2, the reaction is a barrier-free exothermic reaction, and the molar constant volume heat of reaction ((rUm) and molar heat of reaction ((rHm) at normal temperature and pressure are －41.3 and －32.3 kJ mol-1, and the molar Gibbs free energy of reaction ((rGm) is －8.3 kJ mol-1. The second is that the INT1 isomerizes to a three-membered Sn-heterocyclic ring product P1 via a transition state TS1 with an energy barrier of 140.2 kJ mol-1. According to Fig. 2 and Table 2, the reaction is an endothermic reaction, and the (rUm and (rHm at normal temperature and pressure are 128.9 and 126.7 kJ mol-1, and the (rGm is 140.6 kJ mol-1. So, INT1 → P1 is thermodynamically forbidden at normal temperature and pressure, and reaction (1) will end in INT1.

According to Fig. 2, it can be seen that reaction (2) consists of three steps: the first one is that the two reactants (R1, R2) form an intermediate (INT1)[ the situation is the same as reaction(1)]. The second is that the INT1 isomerizes to a four-membered ring stannylene (P2) via a transition state TS2 with an energy barrier of 47.5 kJ mol-1. According to Fig. 2 and Table 2, the reaction is an exothermic reaction, and the (rUm and (rHm at normal temperature and pressure are 116.9 and 110.2 kJ mol-1, and the (rGm is -91.2 kJ mol-1. The third is that the P2 undergoes H transfer via transition state TS2.1 with energy barriers of 282.1 kJ/mol, resulting in the formation of product P2.1. According to Fig. 2 and Table 2, the reaction is an endothermic reaction, and the (rUm and (rHm at normal temperature and pressure are 180.0 and 166.6 kJ mol-1, and the (rGm is 164.6 kJ mol-1. So, P2 → P2.1 is thermodynamically forbidden at normal temperature and pressure, and reaction (2) will end in P2. Comparing reaction (2) with reaction (1), INT1→P1 is thermodynamically forbidden, so reaction (2) will be the dominant reaction channel.

In reaction (3), the four-membered ring stannylene (P2) further reacts with ethylene (R2) to form a spiro-Sn-heterocyclic ring compound (P3). According to Fig. 2, it can be seen that the process of reaction (3) is as follows: on the basis of P2 formed in the reaction (2), it further reacts with ethene (R2) to form an intermediate (INT3). According to Fig. 2 and Table 2, the reaction is a barrier-free exothermic reaction, and the (rUm and (rHm at normal temperature and pressure are －31.4 and －24.0 kJ mol-1, and the (rGm is －14.4 kJ mol-1. Then intermediate (INT3) isomerizes to a spiro-Sn-heterocyclic ring compound (P3) via a transition state (TS3) with an energy barrier of 56.3 kJ mol-1. According to Fig. 2 and Table 2, the reaction is an endothermic reaction, and the (rUm and (rHm at normal temperature and pressure are 40.8 and 39.5 kJ mol-1, and the (rGm is 63.4 kJ mol-1. According to Fig. 2, reaction (3) and P2→P2.1 in reaction (2) are competitive reactions. Due to P2→P2.1 is thermodynamically forbidden, so reaction (3) will be the dominant reaction channel.

In the reaction (3), since (rGm of P2+R2→P3 is 49.0 kJ mol-1, it is a thermodynamically forbidden reaction at normal temperature and normal pressure. In order to carry out the reaction, according to the following thermodynamic formula :

At a temperature of 298 K, P2+R2→P3 is allowed to proceed, and the pressure of the reaction system must be greater than 150325 Pa (1.5 atm).

According to all analyses, reaction (3) should be the dominant reaction channel of the cycloaddition reaction between singlet H2C=Sn: and ethylene, namely:

In this reaction, the frontier molecular orbitals of R1, R2, and P2 are shown in Fig. 3. According to Fig. 3,

Fig. 3. The frontier molecular orbital of R1, R2, P2

the mechanism of reaction (3) could be explained with the frontier molecular orbital diagrams (see Figs. 4 and 5). According to Figs. 1 and 4, when H2C=Sn: (R1) initially interacts with ethylene, 5p unoccupied orbital of tin sidewise overlap with bonding π orbital of ethylene, leading to the formation of a intermediate (INT1). As the reaction goes on, the Sn-C(2) bond(INT1: 2.886 Å, TS2: 2.388 Å, P2: 2.217 Å) , ∠C(1)SnC(2)C(3)（INT1: 88.0°,TS2: 50.0°, P2: 24.6°）and ∠C(1) Sn C(2) (INT1: 81.5°, TS2: 79.5°, P2: 65.6°) gradually decreases, and the C(1)-Sn and C(2)-C(3) bond(INT1: 2.011Å, 1.353 Å; TS2: 2.076 Å, 1.418 Å; P2: 2.217 Å, 1.546 Å) gradually lengthen. Before the transition state (TS2), Sn and C(2) to form a covalent bond. After the transition state (TS2), C(1) and C(3) to form a covalent bond. Thus, INT1 isomerizes to a four-membered ring stannylene (P2) via transition state (TS2). Because P2 is still an active molecular, P2 may further react with ethylene to forms a spiro-Sn-heterocyclic ring compound (P3). The mechanism of this reaction can be explained with the Figures 5 and 1. According to the rule of the molecular orbital symmetry adaptation, when P2 interacts with ethylene (R2), the 5p unoccupied  orbital of the Sn atom in P2 insert the ( orbital of ethylene forms a (→p donor-acceptor bond, leading to the formation of a intermediate (INT3). As the reaction goes on, the Sn-C(4) and Sn-C(5) bond（INT3: 3.030 Å, 2.922 Å ; TS3: 2.241 Å ,2.168 Å; P3: 2.126Å, 2.126 Å）gradually decreases, and the ∠C(2)SnC(4) (INT3: 85.8°, TS3: 113.2°, P3: 138.2 °) gradually increases, the C(4)-C(5) bond（INT3: 1.349 Å，TS3: 1.485 Å , P3: 1.554Å）gradually lengthens. Before the transition state (TS3), the covalent bond is formed between Sn and C(4), Sn and C(5). After the transition state (TS3), the INT3 further isomerises to a spiro-Sn-heterocyclic ring compound(P3) via transition state (TS3). Sn in the spiro-Sn-heterocyclic ring compound is combined with adjacent atoms by sp3 hybridization.

4. Conclusion

According to the potential energy profile, the cycloaddition reaction between singlet H2C=Sn: and ethylene obtained with the MP2/GENECP(C, H in 6-311++G** ; Sn in LanL2dz) method can be predicted. This reaction has one dominant channel. It consists of four steps: (1) the two reactants first form an intermediate (INT1) through a barrier-free exothermic reaction of 41.3 kJ mol-1; (2) the intermediate (INT1) isomerizes to a four-membered ring stannylene (P2) via transition state (TS2) with an energy barrier of 47.5 kJ mol-1; (3) the four-membered ring stannylene (P2) further reacts with ethylene (R2) to form another intermediate (INT3) through a barrier-free exothermic reaction of 31.4 kJ mol-1; and (4) intermediate (INT3) isomerizes to a spiro-Sn-heterocyclic ring compound (P3) via a transition state (TS3) with an energy barrier of 56.3 kJ mol-1. At a temperature of 298 K, the reaction is carried out, and the pressure of the reaction system needs to be greater than 150325 Pa (1.5 atm).

The 5p unoccupied orbital of Sn: in X2C=Sn: is the subject in cycloaddition reaction of X2C=Sn: and the symmetric π-bonded compounds. The 5p unoccupied orbital of tin in H2C=Sn: sidewise overlap with bonding π orbital of ethylene resulting in the formation of an intermediate. Instability of the intermediate make it isomerises to a four-membered ring stannylene. Because the 5p unoccupied orbital of Sn: atom in the four-membered ring stannylene and the π orbital of symmetric π-bonded compounds forms a (→p donor–acceptor bond, the four-membered ring stannylene further combines with symmetric π-bonded compounds to form another intermediate, and the intermediate further isomerises to a spiro-Sn-heterocyclic ring compound. Sn in the spiro-Sn-heterocyclic ring compound is combined with adjacent atoms by sp3 hybridization.

References

# 1. P. J. Stang, Chem. Rev. 78 (1978) 383( https://doi.org/10.1021/cr60314a003)

# 2. P. J. Stang, Acc. Chem. Res. 15 (1982) 348( https://doi.org/10.1021/ar00083a002)

3. H. Leclercq, I. Dubois, J. Mol. Spectrosc 76 (1979) 39 (https://doi.org/10.1016/0022-2852(79)90216-9)

4. R. Srinivas, D. Sulzle, H. Schwarz, J. Am. Chem. Soc. 113 (1991) 52 (https://doi.org/10.1021/ja00001a

010)

5. W. H. Harper, E. A. Ferrall, R. K. Hilliard, S. M. Stogner, R. S. Grev, D. J. Clouthier, J. Am. Chem. Soc. 119 (1997) 8361 (https://doi.org/ 10.1021/ja9716012)

6. D. A. Hostutler, T. C. Smith, H. Y. Li, D. J. Clouthier, J. Chem. Phys. 111 (1999) 950 (https://doi.org/10.1063/1.479187)

7. X. H. Lu, Y. H. Xu, H. B. Yu, W. R. Wu, J. Phys. Chem. A 109 (2005) 6970 (https://doi.org/10.1021/jp05

15075)

8. X. H. Lu, Z. X. Lian, Y. Q. Li, J. Serb. Chem. Soc. 76 (2011) 743 (https://doi.org/10.2298/JSC10082006

5L)

9. X. H. Lu, J. H. Han, Z. X. Lian, Y. Q. Li, J. Serb. Chem. Soc. 76 (2011) 1395 (https://doi.org/10.2298JS

C10092112)

10. X. H. Lu, L. Y. Shi, Y. Q. Li, Z. N. Wang, J. Serb. Chem. Soc. 77 (2012) 75 (https://doi.org/10.2298/

JSC110115119L)

11. X. H. Lu, J. J. Ming, J. Serb. Chem. Soc. 81 (2016) 633 (https://doi.org/10.2298/JSC151130014L)

12. X. H. Lu, Y. H. Xu, L. Y. Shi, J. F. Han, Z. X. Lian, J. Organomet. Chem. 694 (2009) 4062 (https://doi.

org/10.1016/j.jorganchem.2009.08.023)

13. X. H. Lu, L. Y. Shi, J. J. Ming, Arabian. J. Chem. 9 (2016)163 (http://doi.org/10.1016/j.arabjc.2015.02.

001)

14. L. A. Curtis, K. Raghavachari, J. A. Pople, J. Chem. Phys. 98 (1993) 1293 (https://doi.org/10.1063/1.46

4297)

15. K. Fukui, J. Phys. Chem. 74 (1970) 4161 (https://doi.org/10.1021/j100717a029)

16. K. Ishida, K. Morokuma, A. Komornicki, J. Chem. Phys. 66 (1977) 2153 (https://doi.org/10.1063/1.434

152)

Submitting journal name：JOURNAL OF THE SERBIAN CHEMICAL SOCIETY

Title of the article: Ab initio study of mechanism of forming a spiro-Sn-heterocyclic ring

compound by cycloaddition reaction of H2C=Sn: and ethylene

(This paper has 11 pages, 5 figures and 2 table)

Corresponding author: Prof. Xiaojun Tan and Prof. Xiuhui Lu

School of Chemistry and Chemical Engineering

University of Jinan, Jinan 250022,  P. R. China.

E-mail: lxh@ujn.edu.cn

Telephone: +86-0531-82769853

# Text boxes

Fig. 4. A schematic interaction diagram

for the frontier orbitals of H2C＝Sn: (R1) and C2H4 (R2)

Fig. 5. A schematic diagram for the frontier

orbitals of P2 and C2H4 (R2)